## Slide 1: Accelerate Neural networks in resource-limited platforms
Peize LIU
Robotics Institute
Hong Kong University of Science and Technology

## Slide 2: Outline
Our Swarm system progress
Acceleration skills in Neural networks implementation

## Slide 3: Progress in Swarm System
Fully automatic CI-CD system and firmware distribution network

## Slide 4: Progress in Swarm System
Fully automatic self-heal mesh network: Distributed and Decentralized [1]
Dense:
High-speed point-to-point transportation d2vins localization
Low latency
Only cover a small area (only in ideal experiments)
Spars
Low-speed data transportation
High latency
Large area
[1]: https://www.open-mesh.org/projects/batmand/wiki/VisualizeMesh

## Slide 5: Progress in Swarm System
More refined photometric calibration for fisheye cameras[1]
[1]:Direct spase Odometry: Jakob Engel, Vladlen Koltun, Daniel Cremers https://cvg.cit.tum.de/_media/spezial/bib/bergmann17calibration.pdf
[2]:https://github.com/tum-vision/mono_dataset_code/tree/master
[3]:https://github.com/gaowenliang/vignetting_calib (William Gao version)
Original Version
DSO Version
Good with this version

## Slide 6: Omnidirectional Depth estimation
Four fisheye cameras with FOV up to 220 deg
Eight virtual pinhole cameras with FOV 95 deg
Photometric uncalibrated
Photometric calibrated

## Slide 7: Scenario

## Slide 8
HITNET[1] 240x320 fp16 optimized
[1]: HITNet: Hierarchical Iterative Tile Refinement Network for Real-time Stereo Matching, Vladimir Tankovich,Christian Häne ,.etc

## Slide 9
CREStereo[1] 240x320 fp16 optimized
[1]: Practical Stereo Matching via Cascaded Recurrent Network with Adaptive Correlation: Jiakun Li Peisen Wang, etc.

## Slide 10: Inference time comparison
Chart: Jetson Orin 100TOPS (ms) HITNET 240x320
| Batch 1 | Batch 4 | stream 1 | stream 4
CUDA | 160 | 400 | 160 | 200
Tensorrt | 80 | 210 | 80 | 90
trt+Int8 | 70 | 205 | 70 | 65
trt+int8+fp16 | 50 | 195 | 50 | 62

## Slide 11: How to accelerate inference speed
Current workflow
Jetson Orin
Pytorch
ONNX
TensorRT

## Slide 12: Workflow
Pytorch: layer design should consider TensorRT-supported operators
e.g.
einsum(x,x,x) not supported
einsum(x,x) supported!
Pytorch: layer design should consider using layers that can be accelerated via DLA cores[1]
[1]: https://docs.nvidia.com/deeplearning/tensorrt/developer-guide/index.html#dla_layers
Quantization: Prepare enough calibration datasets(training data instead) to calibrate the model in INT8 inference accuracy/ fp16 acceleration can be performed by tensorrt tool

## Slide 13: Should I do batch or multi-streams
Inference one block takes time t
Inference all takes 4*t
Inference one block takes time t,
inference four streams need 1.5t
Like FDM and TDM in the communication area
Jetson Orin

## Slide 15: Is that still the same for 2080TI or 4090?

## Slide 16
Thanks for your Listening